HamComm 3.1                  Manual               June 10. 1996






















                                     HamComm
                                   Version 3.1


                                  June 10. 1996




                                 W. F. Schroeder

                                      DL5YEC




























                                        1



         HamComm 3.1                  Manual               June 10. 1996


                                Table of contents

         1 Introduction ...............................................4
         2 License ....................................................4
         3 Update .....................................................4
         4 Exclusion of warranty ......................................5
         5 System requirements ........................................5
         6 Installation ...............................................5
         7 Startup ....................................................6
         8 Config file HC31.CFG .......................................6
         9 Screen layout ..............................................7
         10 Help system ...............................................7
         11 File menu .................................................7
           11.1 Start RX logging ......................................7
           11.2 Save RX Win & log .....................................8
           11.3 Start/Stop TX logging .................................8
           11.4 Log to printer ........................................8
           11.5 Macro recorder ........................................8
           11.6 Load macros ...........................................8
           11.7 Save macros ...........................................8
           11.8 Load config file ......................................9
           11.9 Send text file ........................................9
           11.10 About HamComm ........................................9
           11.11 Shell to DOS .........................................9
           11.12 Exit to DOS ..........................................9
         12 Mode menu .................................................9
           12.1 TX on/off .............................................9
           12.2 CW ....................................................9
           12.3 Baudot ................................................9
           12.4 ASCII 7/8 ............................................10
           12.5 AMTOR Listen .........................................10
           12.6 AMTOR ARQ ............................................10
           12.7 AMTOR FEC ............................................10
           12.8 Pactor Listen ........................................10
           12.9 Bit Length ...........................................11
           12.10 Spectrum ............................................11
           12.11 Scope ...............................................11
           12.12 Tune ................................................11
         13 Speed menu ...............................................11
           13.1 Baud selection .......................................11
           13.2 WPM selection ........................................11
           13.3 RX AutoWPM ...........................................11
         14 Keying menu ..............................................12
           14.1 Normal/Reverse .......................................12
           14.2 170Hz, 425Hz, 850Hz, Set var .........................12
           14.3 Diddle ...............................................12
           14.4 Clear TX Buffer ......................................12
           14.5 External Converter ...................................12
           14.6 AFC ..................................................12
         15 Port menu ................................................12
           15.1 COM1 - COM4 ..........................................12
           15.2 Use Speaker ..........................................12
         16 Text menu ................................................13
           16.1 Send Text ............................................13
           16.2 Define Text ..........................................13
           16.3 Define Call/Name/Selcall .............................13
           16.4 Set QSO count ........................................13
           16.5 Send QSO count .......................................13
           16.6 Advance and send QSO count ...........................13

                                        2



         HamComm 3.1                  Manual               June 10. 1996

           16.7 AMTOR AAB ............................................13
           16.8 AutoUnshift ..........................................13
           16.9 Blank lines ..........................................13
           16.10 Extended Baudot .....................................14
           16.11 Word/Character mode .................................14
           16.12 WX decoder ..........................................14
           16.13 Force SHIP/SYNOP decode .............................15
         17 Info menu ................................................15
           17.1 Locator ..............................................15
           17.2 Callsign .............................................15
           17.3 HamComm ..............................................15
           17.4 System ...............................................15
         18 Options menu .............................................15
           18.1 Clear RX/TX window ...................................15
           18.2 Set ClockCorr ........................................15
         19 Interface schematics .....................................16
         20 Receive circuit ..........................................16
         21 PTT circuit ..............................................16
         22 Transmit circuit .........................................17
         23 External converter .......................................17
         24 External AFSK ............................................17
         25 Signal decoding ..........................................18
         26 RTTY Basics ..............................................18
         27 RTTY Decoding ............................................19
         28 Morse code basics ........................................19
         29 Morse code decoding ......................................20
         30 SITOR A/B ................................................21
         31 NAVTEX ...................................................21
         32 AMTOR ....................................................22
         33 FEC monitoring ...........................................22
         34 FEC transmission .........................................23
         35 ARQ LISTEN mode ..........................................23
         36 ARQ transmission .........................................23
         37 Error correction .........................................24
         38 Clock correction .........................................25
         39 Macro keys ...............................................26
         40 SHIP/SYNOP decoder .......................................26
         41 Scope function ...........................................28
         42 Spectrum function ........................................29
         43 Bitlength statistics .....................................30
         44 Interface checkout .......................................31
         45 Port address .............................................31
         46 Op-Amp power supply ......................................32
         47 IRQ number ...............................................34
         48 Appendix A - Key assignment summary ......................35
         49 Appendix B - Baudot code table ...........................38
         50 Appendix C - Interface schematics ........................39
         51 Appendix D - Interface supplier ..........................41
         52 Index ....................................................42












                                        3



         HamComm 3.1                  Manual               June 10. 1996



         1 Introduction

         HamComm is a program for ham radio communications.  Version 3.1
         supports reception and transmission of radio teletype and Morse
         code  signals.    Available  modes  are  BAUDOT,  ASCII,  AMTOR
         ARQ/FEC, SITOR  A/B  and NAVTEX.    For PACTOR  transmission  a
         'Listen' mode is  available.   Weather station  reports in  the
         SHIP and SYNOP format can also be decoded.

         A conventional converter or  modem chip is  not required.   The
         audio output of the receiver is connected to the serial port of
         a PC-compatible computer thru  a very simple low-cost  circuit.
         Only one inexpensive IC is needed (Op-Amp TL071 or similar) and
         a few  diodes,  capacitors and  resistors.   A  separate  power
         supply is not required,  the supply current  is drawn from  the
         serial port.    For  transmission the  audio  signal  from  the
         speaker or serial port is connected to the microphone input  of
         the transmitter thru  a passive  R/C filter.   Audio  frequency
         generation and  decoding,  serial/parallel conversion  and  all
         other signal processing is done by the program.


         2 License

         HamComm 3.1 is not a "public domain" program.

                    Copyright (c) 1990-1996 by W.F. Schroeder
                               All rights reserved.

         HamComm  3.1 is  shareware.   The unregistered  version may  be
         freely copied and distributed.   The program and/or manual  may
         not be modified in any way without the prior written permission
         by the author.  It is not allowed to charge more than US$10 for
         distribution.

         You are hereby granted a limited  license to use this  software
         for evaluation purposes for a period of 30 days.  If you intend
         to continue using  this software  after the  30 day  evaluation
         period, you must make a registration  payment of US$30 or  DM40
         to:

              W. F. Schroeder
              Augsburger Weg 63
              D-33102 Paderborn
              Germany

         Please note: the bank will  charge a fee up  to DM10 to cash  a
         cheque drawn on a foreign (non-german) bank.  For this reason i
         can only  accept cheques  about DM40  drawn on  a german  bank.
         Alternatively you can send an international postal money  order
         or banknotes (DM or equivalent amount in local currency).


         3 Update

         For registered  users  of  previous versions,  HamComm   3.1 is
         available for DM15 in Germany or US$15 to all other countries.


                                        4



         HamComm 3.1                  Manual               June 10. 1996



         4 Exclusion of warranty

         The author  provides  absolutely  no warranty,  to  the  extent
         permitted by  applicable  state  law.   Except  when  otherwise
         stated in writing, the author and/or other parties provide this
         program "AS IS" without warranty of any kind, either  expressed
         or  implied,  including,  but  not  limited  to,  the   implied
         warranties of  merchantability  and fitness  for  a  particular
         purpose.  The entire risk as to the quality and performance  of
         the program is with you.   Should the program prove  defective,
         you assume  the  cost of  all  necessary servicing,  repair  or
         correction.

         In no event unless required by  applicable law will the  author
         and/or any other party who may modify and/or redistribute  this
         program be  liable  to  you for  damages,  including  any  lost
         profits,  lost  monies,   or  other   special,  incidental   or
         consequential damages arising  out of the  use or inability  to
         use (including but not  limited to loss of  data or data  being
         rendered inaccurate or losses sustained  by third parties or  a
         failure of the program to operate with any other programs) this
         program, even if you  have been advised  of the possibility  of
         such damages, or for any claim by any other party.


         5 System requirements

         HamComm  3.1 will run  under MS-DOS  3.x or  higher on  any PC-
         compatible computer  with at  least 400KB  of free  memory.   A
         harddisk is highly  recommended.  Because  of the  size of  the
         program file there may be not enough space to copy all required
         files onto a 720KB diskette.   On slow systems, e.g. 8088  CPU,
         some functions may not work as expected or may not work at all.

         HamComm will automatically detect the type of video adapter  in
         use.   MDA, CGA,  EGA, VGA  and Hercules  are supported.    The
         graphics display functions are not available on MDAs since  the
         MDA has no graphics  mode.  No attempt  has been made to  avoid
         screen flicker (snow) on cheap CGAs.

         HamComm will probably  not run under  any kind of  multitasking
         software like  Desqview, Windows  3.x/95/NT  or OS/2  since  it
         requires direct control of the interrupt controller, timer chip
         and serial I/O hardware.


         6 Installation

         For installation on a harddisk you should create a subdirectory
         `HAMCOMM' and change to that directory.  HamComm is distributed
         as a .ZIP  or .EXE  file.  To  unpack a  .ZIP file  you need  a
         program like UNZIP or  PKUNZIP.  The .EXE  version is a  'self-
         extracting archive' which contains all the files and a build-in
         unpack program.   In  both cases  the extracted  files will  be
         placed in the current directory.

         Please read the files README, HC31.CFG and CHANGES !


                                        5



         HamComm 3.1                  Manual               June 10. 1996



         7 Startup

         To start HamComm type HC at the DOS prompt and hit ENTER.   The
         interface circuit is not needed if  you just want to play  with
         the program.

         HamComm  3.1 normally  uses  the video  mode  with the  maximum
         number of lines, e.g. 50 lines on  VGA, 43 lines on EGA and  25
         lines with other video cards.  If  you want to use a mode  with
         less line, specify option ` -L43' to switch to 43 lines  on VGA
         cards or `-L25' for 25 lines on EGA/VGA cards.

         Many SuperVGA  cards have  special text  modes e.g.   80x60  or
         132x44.   Activate the  desired mode  before starting  HamComm.
         Most cards come with  a utility program to  do this.  Only  the
         modes where the video display buffer starts at segment B800 are
         supported.  Start HamComm with the commandline option `-LX' for
         automatic  determination  of  the  number  of  text-lines   and
         columns.  Some  mouse drivers have  problems with the  extended
         text modes,  as they  are not  smart  enough to  recognize  the
         screen dimensions.

         HamComm assumes  that the  original  PC display  character  set
         known as "codepage 437" is active.

         On startup the program identifies the video card and monitor in
         use and  automatically selects  the graphics  mode for  highest
         resolution.  Some program functions require a graphics mode for
         display of the input signal.

         The identification may fail because of compatibility  problems.
         By selecting one of  the following commandline options  HamComm
         can be forced to use the specified mode:

              Option     Mode        Resolution

              -cga       6           640x200  2-color
              -ega       10h         640x350 16-color
              -vga       12h         640x480 16-color
              -herc      Hercules    720x348  2-color

         If you have a computer with  an LCD display and readability  is
         poor try the following DOS command before starting HamComm:

              mode bw80

         The 'mode' program is supplied with MS-DOS and is used here  to
         switch to black and white mode.


         8 Config file HC31.CFG

         When HamComm is started the program automatically searches  for
         a configuration file called "HC31.CFG".  The current  directory
         is searched first, then all other directories along the current
         "PATH".  The supplied HC31.CFG file  is an ASCII text file  and
         can be sent to a printer or changed with a text editor.  Please
         take the  time  to read  it  carefully and  make  the  required

                                        6



         HamComm 3.1                  Manual               June 10. 1996

         adjustments for your  system.  At  least you should  substitute
         DL5YEC with your own callsign.

         HC31.CFG includes explanations and  examples for all  available
         configuration commands.   It  is only  special  in that  it  is
         executed automatically on program startup.  You can also  write
         your own .CFG files and execute  them from the FILE menu  while
         running HamComm.  This could be used to set several  parameters
         like Baud and shift to special  values in one step.  You  could
         also build a set  of .CFG files for  loading standard texts  in
         different languages.  In combination  with the macro keys  they
         could then be loaded with a single key.


         9 Screen layout

         HamComm has an  SAA-like user interface  with pull-down  menus,
         dialog boxes and online helptexts.  The menu bar at the top  of
         the screen is always visible while the display is in text mode.
         The bottom line  has information about  the currently  selected
         menu item.

         Every name on the menu bar has a highlighted character.   Press
         and hold the  ALT key  and type  that character  to select  the
         corresponding menu.  The cursor-left and cursor-right keys  can
         now be  used to  switch to  the previous/next  menu.   Use  the
         cursor-up and cursor-down keys to move to the desired  function
         and hit the  ENTER key.   Selecting a mode  from the mode  menu
         will get you to the main transmit/receive (RX/TX) screen.

         Every menu line also has a highlighted character.  Typing  that
         character (without the ALT  key) will get  you directly to  the
         corresponding function.

         Some  frequently  used  menu  entries  have  been  assigned  to
         function keys.   The  F8 key  for example  activates the  SCOPE
         function.

         The ESC  key  can  be  used  at any  time  to  abort  the  menu
         selection.


         10 Help system

         The ALT-H  and F1  keys both  start the  help system  but  show
         different kinds of information.  The ALT-H key displays general
         information about the program, the F1 key displays a help  text
         specific to the current situation.



         11 File menu

         11.1 Start RX logging

         The text appearing  in the receive  window can be  logged to  a
         file.  You will be asked to enter the name of the logfile  with
         a suggested file type of  ``.LOG``.  If the  logfile is active,
         its name is displayed on the upper left border of the  transmit
         window.  The text of the entry  in the FILE menu is changed  to

                                        7



         HamComm 3.1                  Manual               June 10. 1996

         ``Stop RX logging`` and it will close the  logfile if selected.
         The  file  will  also   be  closed  automatically  on   program
         termination.

         Whenever a new  line begins in  the logfile,  the text  element
         `logrxlabel'  is  inserted  in   receive  mode  and  the   text
         `logtxlabel' is inserted  in transmit mode.   See the  supplied
         configuration file   HC31.CFG for  a  sample  definition  which
         inserts the current time.

         This menu entry is only available after selecting an  operating
         mode from the MODE menu.


         11.2 Save RX Win & log
         This entry is almost identical to `Start RX logging'  described
         above.  The  contents of  the RX window  is saved  to the  file
         before the normal logging operation begins.

         This menu entry is only available after selecting an  operating
         mode from the MODE menu.


         11.3 Start/Stop TX logging
         Open/Close the logfile for the TX window.


         11.4 Log to printer
         All text  appearing in  the RX  window will  be copied  to  the
         device PRN which is normally connected to LPT1.  Make sure that
         the printer is ready to print  before activation.  A  checkmark
         is displayed in front of the menu entry while logging.


         11.5 Macro recorder
         This menu  entry is  used to  start the  recoder for  keystroke
         sequences which can be assigned to and replayed with the  macro
         keys.   Please  refer to  section  `Macro keys'  (p. 26) for  a
         detailed discussion


         11.6 Load macros
         To load  a previously  saved  ``.MAC``macro  file select  "Load
         macros" from the FILE menu.  All macro definitions found in the
         selected  file  will  be  added  to  or  replace  the   current
         assignments.  Macro keys that didn't hold any keystrokes at the
         time the file was written, will not be changed when the file is
         loaded.

         There is also a way to  load your favourite macros  definitions
         automatically.  When  HamComm is  started it  searches for  the
         default macro file HC.MAC, first in the current directory, then
         in every directory along the PATH.


         11.7 Save macros
         Macro definitions can  be saved to  a file  by selecting  "Save
         macros" from the FILE menu.  The usual file select box pops  up
         with a  suggested   .MAC file  type.    All recorded  keystroke
         sequences will be saved to the selected file.

                                        8



         HamComm 3.1                  Manual               June 10. 1996



         11.8 Load config file
         This menu entry  is used to  select and  process config  files.
         The file select box shows the  .CFG files found in the  current
         directory.  Enter the name of the file to be processed or  pick
         one from the list.


         11.9 Send text file
         The text  from the  selected file  will be  transferred to  the
         transmit buffer.

         This menu entry is only available after selecting an  operating
         mode from the MODE menu.


         11.10 About HamComm
         This command displays the program date and version.


         11.11 Shell to DOS
         This menu entry starts a copy  of the DOS command  interpreter.
         HamComm remains in memory and the receive and transmit routines
         continue to execute  in the background.   The available  memory
         will usually be  very limited, so  only small  programs can  be
         run.


         11.12 Exit to DOS
         Terminates the program and returns to DOS.  Transmit mode  will
         be terminated and any open files will be closed.



         12 Mode menu

         12.1 TX on/off
         This command switches  from receive to  transmit mode and  vice
         versa.   The same  function is  assigned to  the Control-T  key
         while the RX/TX screen is active.


         12.2 CW
         Activates  the  RX/TX  screen  and  selects  the  CW  mode  for
         reception and transmission of Morse code.   See the SPEED  menu
         for automatic  or manual  speed adjustment.   The  current  WPM
         (Words Per  Minute)  setting  is shown  at  the  bottom  window
         border.  For more  information see the  sections on Morse  code
         basics (p.19) and decoding.


         12.3 Baudot
         Activates the RX/TX screen and  selects the 5-bit Baudot  code.
         Select other  required parameters  from  the SPEED  and  KEYING
         menus.  For more  information see the  sections on RTTY  basics
         (p.18) and decoding.




                                        9



         HamComm 3.1                  Manual               June 10. 1996



         12.4 ASCII 7/8
         These commands are  similar to the  Baudot selection above  but
         use the 7-bit ASCII code or the PCs extended 8-bit code.  ASCII
         mode is rarely  used and  was only  included for  completeness.
         Tuning, speed selection and keying direction are done just like
         with the Baudot mode.


         12.5 AMTOR Listen
         AMTOR  Listen   mode  is   used   for  monitoring   AMTOR   ARQ
         transmissions from  ham radio  stations and  SITOR A  used  for
         maritime communications.  See  the sections 'AMTOR' (p. 22) and
         'ARQ LISTEN mode' (p.23) below for more information.


         12.6 AMTOR ARQ
         Select this menu entry  for two-way communication with  another
         AMTOR station.   The  program checks  the received  signal  and
         automatically responds to incoming ARQ  calls.  To initiate  an
         AMTOR link enter the SELCALL of the other station from the TEXT
         menu and then  switch to  TX mode.   See  the sections  'AMTOR'
         (p.22)  and   'ARQ   transmission'  (p. 23)  below   for   more
         information.


         12.7 AMTOR FEC
         AMTOR FEC mode is mainly used by radio amateurs for calling  CQ
         (call to all stations), but also by coast stations for  weather
         broadcasts and traffic lists.  The speed is always 100 Baud and
         is set internally.  Set the keying direction to `normal' on USB
         and `reverse' on LSB.  For more information see the sections on
         `FEC monitoring' (p.22) and `FEC transmission' (p.23) below.


         12.8 Pactor Listen
         This mode is  used for  monitoring Pactor  transmissions.   The
         speed is normally 200 Baud but drops back to 100 Baud under bad
         conditions.  The  speed and  the keying  direction is  detected
         automatically, so  you only  have to  tune in  to the  station.
         Pactor FEC, which is  used for calling CQ,  has the same  frame
         structure as the Pactor ARQ mode and will also be decoded.

         Pactor uses a  CRC checksum for  error detection and  sometimes
         Huffman compression for higher thruput.  Unlike with AMTOR  ARQ
         damaged frames can not be decoded in part, so you either get  a
         perfect copy or miss the frame completely.  If HamComm  detects
         a missing frame it displays a dot and starts a new line.

         The status  field  in  the lower  left  corner  has  a  quality
         indicator (0 - 4 for 200 Baud, 0 - 9 for 100 Baud), the  letter
         `H' to indicate  Huffman encoding, the  speed (100/200) of  the
         last decoded frame and the status byte from the last frame with
         the frame number.






                                        10



         HamComm 3.1                  Manual               June 10. 1996



         12.9 Bit Length
         Changes to  the  graphics screen  for  `Bitlength  statistics'.
         This display  is  used  to  check  the  speed  of  the  decoded
         mark/space signal for Baudot and ASCII transmissions.  See  the
         section `Bitlength statistics' (p.30) for more information.


         12.10 Spectrum
         Changes to the `Spectrum'  screen.  This  display has the  best
         frequency resolution  and can  therefore  be used  for  precise
         tuning and to measure  the shift of the  received signal.   See
         the section `Spectrum function' (p.29) for more information.


         12.11 Scope
         Changes to the `Scope' screen, a graphics display of the signal
         frequency versus time.  See the section `Scope function' (p.28)
         for more information.


         12.12 Tune
         The `Tune' screen is used to  set the center frequency for  the
         mark and  space tones.   It  also shows  the frequency  of  the
         incoming signal.  To set the  center frequency use the  cursor-
         left/right keys, or click on  the highlighted fields below  the
         scale.    You  can  also  click  on  the  lower  scale.     The
         LOWER/HIGHER  fields  move   the  center  frequency   indicator
         left/right.  Click on the RESET field or hit the `Home' key  to
         restore the last  value set from  a .CFG file.   There are  two
         more fields for predefined values of 1360Hz and 2210Hz.



         13 Speed menu

         13.1 Baud selection
         The first part  of the  SPEED menu  selects the  speed for  the
         asynchronous modes Baudot  and ASCII.   Pick a  speed from  the
         predefined values  or enter  it directly  using the  `Set  var'
         entry.  The speed for the synchronous modes AMTOR and Pactor is
         part of the transmission protocol and can not be changed.


         13.2 WPM selection
         The second part of the menu selects the speed in WPM (Words Per
         Minute) for the CW mode.


         13.3 RX AutoWPM
         Toggles the automatic  CW speed tracking  while receiving.   If
         this option is  enabled HamComm automatically  adjusts the  WPM
         setting according to  the received  signal.   For manual  speed
         selection disable this option and select the desired WPM value.






                                        11



         HamComm 3.1                  Manual               June 10. 1996



         14 Keying menu

         14.1 Normal/Reverse
         These menu  items  select the  keying  direction both  for  the
         received and transmitted signals.  With direction `normal'  the
         higher tone indicates the making (idle) state.


         14.2 170Hz, 425Hz, 850Hz, Set var
         These  menu  items  select  the  shift  for  the  received  and
         transmitted signals.   The  shift is  the frequency  difference
         between the mark and space tones.  Select one of the predefined
         values or enter the desired value using the `Set var' entry.


         14.3 Diddle
         If HamComm runs out of text  while in Baudot or ASCII  transmit
         mode  the  `Diddle'  option   controls  transmission  of   idle
         characters.  If this option is disabled a constant `mark'  tone
         is generated.


         14.4 Clear TX Buffer
         Clears the buffer for outgoing text.


         14.5 External Converter
         If this  option is  enabled, HamComm  will use  the  mark/space
         signal from an external converter for decoding.  The signal  is
         expected at the CTS pin of the selected serial port.


         14.6 AFC
         AFC stands for Automatic Frequency Control.  If this option  is
         activated the center frequency  will be constantly adjusted  to
         track the received signal.  It  can be used for automatic  fine
         tuning or compensation  of receiver  drift.   The AFC  function
         should only be used for modes with a constant tone like Baudot,
         ASCII and AMTOR/Pactor FEC.



         15 Port menu

         15.1 COM1 - COM4
         Selects and initialises the serial port  to be used.  See  also
         the `select port ...' command in HC31.CFG.


         15.2 Use Speaker
         HamComm normally  generates the  transmit tones  using the  TxD
         line of the serial port.  If this option is activated the tones
         are also send to the speaker.






                                        12



         HamComm 3.1                  Manual               June 10. 1996



         16 Text menu

         16.1 Send Text
         Displays a  dialog box  containing all  currently defined  text
         elements.  Select the text to be transmitted and hit the  ENTER
         key or double-click  on the  desired item.   The  text will  be
         transferred to the TX window.  Hit ESC to terminate the  dialog
         box.

         16.2 Define Text
         Defines a text element  `on the fly'.   Enter the text-ID  (the
         name of the text) and the  text string in the displayed  dialog
         box.  Please note that the text will not be saved to disk.   To
         define a permanent text see the examples in file HC31.CFG.


         16.3 Define Call/Name/Selcall
         These menu items also display the `Define Text' dialog box, but
         the text-ID field is preset to `call', `name' or `selcall'.


         16.4 Set QSO count
         Displays a dialog box  where you can set  the value of the  QSO
         counter used from contest operation.


         16.5 Send QSO count
         Transfers the current QSO count to the TX window.


         16.6 Advance and send QSO count
         Increments the QSO counter  by one and  transfers its value  to
         the TX window.


         16.7 AMTOR AAB
         Enable/disable Automatic-Answer-Back for AMTOR ARQ links.  If a
         WRU (Who aRe yoU?)  character is received  during an AMTOR  ARQ
         link and  this  option is  enabled  and the  text  AmtorAAB  is
         defined, the  text will  automatically  be transmitted.    This
         feature is normally used to  automate the login procedure  when
         connecting to an AMTOR mailbox.


         16.8 AutoUnshift
         In Auto-Unshift  mode HamComm  will automatically  switch  from
         figures to  letters in  BAUDOT mode  on  reception of  a  space
         character.


         16.9 Blank lines
         HamComm normally ignores blank lines  to conserve space in  the
         receive window.  If this option is enabled blank lines will  be
         displayed.





                                        13



         HamComm 3.1                  Manual               June 10. 1996



         16.10 Extended Baudot
         HamComm will use the extended Baudot code for AMTOR and RTTY if
         this option is enabled.  Extended Baudot was invented by  Peter
         Martinez, G3PLX, to transfer the full printable ASCII character
         set over AMTOR links.


         16.11 Word/Character mode
         These options select  the entry mode  for the TX  window.   The
         current entry mode can  be LINE, WORD  or CHAR (character)  and
         controls the text transfer from the TX window to the TX buffer.
         The LINE mode is active if  neither WORD mode nor CHAR mode  is
         seleted.

         LINE mode:

              1.  When a  character is typed in  the last position of  a
              line, the last word  on the line will  wrap around to  the
              next line.   The  current  line will  be  send to  the  TX
              buffer,   followed    by    a    Carriage-Return/Line-Feed
              combination.

              2.  When the 'Enter' key is hit, the current line will  be
              send to the TX buffer, followed by a Carriage-Return/Line-
              Feed combination.

         WORD mode:

              1.   The spacebar,  '?' and  the  EOT character  are  word
              terminators.  When a terminator is entered, all characters
              between the cursor and the first terminator to the left of
              the cursor  (or  the left  window  border) will  be  send.
              Thereafter the terminating character  will be send to  the
              TX buffer and the TX window.

              2.  When the 'Enter' key  is hit, all characters from  the
              first terminator to the  left of the  cursor (or the  left
              window border) up to and  including the last character  on
              the line will be send.  Thereafter a Carriage-Return/Line-
              Feed combination will be send to the TX buffer and the  TX
              window.

              3.  When a  character is typed in  the last position of  a
              line, the last word  on the line will  wrap around to  the
              next line.   Only a Carriage-Return/Line-Feed  combination
              will be send to the TX buffer.

         CHAR mode:

              All text will be displayed in  the TX window and put  into
              the TX buffer immediately.


         16.12 WX decoder
         Enables/disables the decoder for weather observation data  from
         SHIP and SYNOP reports.



                                        14



         HamComm 3.1                  Manual               June 10. 1996



         16.13 Force SHIP/SYNOP decode
         Enables the weather decoder and forces the decoder to interpret
         incoming data as SHIP or SYNOP reports.



         17 Info menu

         17.1 Locator
         Calculates the distance and direction  from one QTH locator  to
         another.  A  dialog box appears  with edit fields  for the  two
         locators.  The first field will be preset to the string defined
         by the  text `mylocator'.   See  file HC31.CFG  for samples  of
         predefined texts.

         This function can also be assigned to a mouse button.  See  the
         file HC31.CFG for details.


         17.2 Callsign
         Attempts to find the country  corresponding to a given  amateur
         radio  call  sign.    You  don't  have  to  type  in  the  call
         completely, the first two or three characters will usually do.

         This function can also be assigned to a mouse button.  See  the
         file HC31.CFG for details.


         17.3 HamComm
         Displays information  about  the  current  program  setup  like
         buffer sizes and serial port configuration.


         17.4 System
         Displays information about  the system like  the type of  video
         adapter and remaining free memory.



         18 Options menu

         18.1 Clear RX/TX window
         Clears the contents of the receive or transmit window.


         18.2 Set ClockCorr
         Enter a clock correction value.  This setting is essential  for
         reliable AMTOR operation.  For more information please refer to
         section `Clock correction' (p.25).

         Note that the  value you enter  in the dialog  box will not  be
         saved. .  The dialog was  added to ease the process of  finding
         the proper value for  your PC.  To  make the setting  permanent
         you will have to change the  "set clockcorr .." command in  the
         file HC31.CFG




                                        15



         HamComm 3.1                  Manual               June 10. 1996


         19 Interface schematics

         The interface schematics are included in the online help texts.

           Start the program,
           Hit ALT-H to start the help subsystem,
           Hit the letter 'O' to select topic 'Overview',
           Hit the TAB key to select topic 'Converter' and hit return,
           Scroll the help text using the cursor-up/cursor-down keys and
           read the text.

         Hit ESC to leave the help system.

         See also appendix C for a plain ASCII version.


         20 Receive circuit

         The operational amplifier  (OpAmp) is used  to bring the  audio
         signal from the receiver up to RS232 level.  The supply current
         is drawn from the  DTR and RTS  pins of the  serial port.   The
         four diodes (1N4148 or similar) of  the receive circuit form  a
         standard bridge rectifier.   The  1uF capacitors  are used  for
         buffering.

         The input signal  amplitude should be  at least  100mVpp.   The
         100nF capacitor removes any DC bias.  Since the OpAmp runs with
         maximum gain  there  will  be  a  (more  or  less)  rectangular
         waveform at its  output.   It should  have an  amplitude of  at
         least +/-5V to reliably drive the RS232 input.

         The operational  amplifier  LM741  was choosen  because  it  is
         inexpensive  and  widely  available.     However  with   todays
         technology its electrical characteristics  are not  impressive.
         An LF356 or TL071 for example  is much faster and has a  higher
         input resistance.  If you want to substitute a different  opamp
         type, keep in  mind that  the serial  port can  only deliver  a
         supply current of a few milliamperes.


         21 PTT circuit

         The RTS output of the COM port is not only used to provide  the
         supply current for the opamp, but also to key the  transmitter.
         A Diode  is used  to protect  the base  of the  PTT  transistor
         against the negative voltage of the RTS output in receive mode.
         The resistor  is  required  to limit  the  base  current.    In
         transmit mode the RTS and DTR pins change polarity.  RTS is now
         positive and the transistor pulls the PTT line to ground.  This
         circuit has been  tested with an  FT747, FT757GXII, TS440S  and
         TS-950SD.  On some old rigs there may be a high voltage on  the
         PTT line.  The required current to key the transmitter may also
         be too  high for  a small  transistor, so  better check  BEFORE
         connecting it to the computer.






                                        16



         HamComm 3.1                  Manual               June 10. 1996



         22 Transmit circuit

         AFSK tone signals for transmission are available at two places:

          at the speaker connector
          at the serial port  (recommended)

         With many motherboards one side of the speaker is connected  to
         the +5Volt supply thru a resistor, the other side is pulled  to
         ground by a transistor.  In contrast to most other areas of the
         PC's hardware  there  is no  standard  design for  the  speaker
         output, so there may be variations.  In general one side of the
         speaker will be near ground or +5Volt, while the other side has
         a square-wave signal.  This signal is fed to two R/C filters to
         smooth it out.   The microphone  input is very  sensitive so  a
         variable resistor is  used for attenuation  and a capacitor  to
         remove any DC.

         If you don't want to make any modifications to the PC or if the
         speaker output  is not  accessible, you  can also  get an  AFSK
         signal from the TxD pin of  the COM port.  The frequencies  are
         not quite as accurate as at  the speaker output and will  often
         deviate by 5 to 10Hz, but this usually gives no problems.   The
         signal level at the TxD pin is much higher than at the  speaker
         output, so you may have to change the component values for  the
         R/C filter and the attenuator a bit.


         23 External converter

         An option  "External Converter"  is available  on the  "Keying"
         menu.  It can  also be controlled  by the ALT-F9/ALT-F10  keys.
         If this option is enabled, a mark/space signal from an external
         converter or modem chip is expected  at the CTS pin of the  COM
         port.

         Please note that the HamComm  interface is no longer  required,
         but is highly recommended.  If  you don't use it you loose  the
         SCOPE and  SPECTRUM functions  which are  also very  handy  for
         precise tuning.   Connect the input  of the  converter and  the
         input of  the HamComm  interface in  parallel to  the  receiver
         output.

         Filter  converters   for   RTTY  are   normally   designed   to
         differentiate between two tones.   For CW  reception a kind  of
         tone decoder is required that can tell the tone from noise.


         24 External AFSK

         AFSK tones  for  transmission  are normally  available  at  the
         speaker output or the TxD  pin of the COM  port.  If you  don't
         want to use those signals for whatever reason, you can find  an
         FSK signal  at  the  DTR  pin  of  the  COM  port.    For  RTTY
         transmission DTR is negative for 'mark' state and positive  for
         'space' state.  In  CW mode DTR is  negative for 'no-tone'  and
         positive for 'tone'.  During reception DTR is always positive.


                                        17



         HamComm 3.1                  Manual               June 10. 1996

         Note that in receive  mode the RTS pin  is negative and  always
         positive during transmissions.  It can thus be used to gate the
         DTR signal for keying a transmitter in CW mode.

         If you attach  any additional components  to these pins  please
         keep in mind that the DTR/RTS signals supply the power for  the
         OpAmp.


         25 Signal decoding

         The amplified audio signal is connected to the DSR modem status
         input of the serial port where every zero crossing generates an
         interrupt.   HamComm  determines the  time  between  successive
         interrupts  using  the  Pcs  timer  chip  and  calculates   the
         corresponding tone frequency.  Due  to the timer resolution  of
         about  one  microsecond  the  result  is  quite  accurate   and
         constitutes the base for all further signal processing.

         For RTTY  decoding  the  tone  is  compared  to  the  currently
         selected center frequency to decide wether this is a 'mark'  or
         'space' signal.  The mark/space signal is sampled at the proper
         time according to  the current Baud  collecting all  bits of  a
         character.

         For CW decoding the program has to differentiate the tone  from
         noise.   To be  regarded a  valid  signal the  tone has  to  be
         between the  currently selected  mark/space frequencies  for  a
         certain amount  of  time.   The  program maintains  a  floating
         average of  the length  of the  dots and  dashes to  adjust  to
         varying speeds.

         When the character is  complete it is  converted to ASCII  code
         and displayed in the RX window.


         26 RTTY Basics

         Radio  TeleTYpe  (RTTY)  uses  two  different  tones  for  data
         transmission.  They  are called  the 'mark'  and 'space'  tone,
         where  mark  is  usually  the  higher  tone.    The   frequency
         difference between them is called 'shift'.  Transmission  speed
         is specified in 'Baud',  wich is the  number of signal  changes
         per second.  Ham radio RTTY  normally uses 45 Baud and a  shift
         of 170Hz on shortwave.

         Characters are encoded using ASCII  or the more popular  Baudot
         code.   ASCII  uses  combinations of  7  bits  to  represent  a
         character while  Baudot uses  only 5  bits.   With  two  signal
         states (mark and space) we can only transmit one bit at a time.
         The bits of a  character are therefore  sent one after  another
         starting with the least significant bit.  If the value of a bit
         is 1 then it is represented by the mark tone, otherwise by  the
         space tone.

         The mark tone  is also used  whenever the  transmitter is  idle
         e.g. there is  no character left  in the transmit  buffer.   In
         front of every  character a  single space  bit is  sent.   This
         'start bit'  informs the  receiver that  a   new  character  is


                                        18



         HamComm 3.1                  Manual               June 10. 1996

         coming in.  Next  are the data  bits comprising the  character,
         followed by a 'stop bit' of mark polarity.

                 State                Time -->

                 mark  ------   --------------------------------
                            |Sta|Bit|Bit|Bit|Bit|Bit|Stp|
                            |   | 1 | 2 | 3 | 4 | 5 |   |
                 space      -------------------------

         The duration of a bitcell is 1/Baud.  At 50 Baud a bit is  20ms
         long.


         27 RTTY Decoding

         To decode an RTTY signal the center frequency has to be in  the
         middle between the  mark and space  tones.   Activate the  TUNE
         screen from the MODE menu  or hit F9.   Tune the radio so  that
         the lower tuning bar is between  the two upper tuning bars.  To
         change the center frequency use the arrow keys or the mouse.

                           Signal Frequency: 01### Hz

          0 . . . .500. . . .1000. . . .1500. . . .2000. . . .2500 Hz
                       Space ->   |   |  <- Mark
                                    |

                           Center Frequency: 01360 Hz

         On a fast PC  the SPECTRUM function (F7)  can be used for  more
         precise tuning.  Adjust the radio so that the two peaks of  the
         RTTY signal  match the  marker lines  for  the mark  and  space
         tones.  The mark/space distance (shift) is controlled from  the
         KEYING menu.

         To start the decoder  select Baudot from the  MODE menu or  hit
         F3.  Accurate tuning is essential  but you also have to  select
         the proper speed and keying direction.  Hit Alt-S to select the
         speed.  Ham  RTTY is  usually 45  baud, sometimes  50 baud  and
         outside of the ham bands 50, 75 and 100 bauds are most  common.
         If you  don't  know what  speed  to select  try  the  BITLENGTH
         STATISTICS display (F6).

         Hit the Tab key to toggle between Normal and Inverted keying.

         RTTY is an asynchronous mode.   Sender and receiver don't  keep
         their internal time  references in sync.   The receiver  simply
         waits for  the  leading  edge of  the  startbit,  collects  the
         databits according to the signal speed  and then waits for  the
         next character.


         28 Morse code basics

         Morse code, also known as CW (continuous wave), uses  sequences
         of short and long tones for  character encoding.  A short  tone
         is called a 'dot', a long tone is called a 'dash' and should be
         three times as long as a dot.  The gaps between the tones of  a
         character are as  long as a  dot, the  gaps between  characters

                                        19



         HamComm 3.1                  Manual               June 10. 1996

         should be as long as a dash.  The overall speed of a Morse code
         transmission is  measured in  'words  per minute'  (WPM)  while
         sending the word 'PARIS'.

         Characters occuring very often in a  text are encoded as  short
         sequences, seldomly  used  characters are  assigned  to  longer
         sequences.  The letter 'E' for example is just one dot (.), 'T'
         is one dash (-) and the letter 'Q' is dash-dash-dot-dash  (--.-
         ).

         Morse code is  used for example  by maritime  services and  ham
         radio operators.  Try the lower end of the amateur 80m, 40m and
         20m bands starting at 3.5MHz, 7MHz and 14mhz.


         29 Morse code decoding

         To decode a CW  transmission the tone  frequency of the  signal
         should closely match the  currently selected center  frequency.
         Activate the TUNE screen  from the MODE menu  or hit F9.   Tune
         the radio so that the upper  bar indicating the signal tone  is
         lined up with the  lower bar.  To  change the center  frequency
         use the arrow keys or the mouse.

         Signal Frequency: 01### Hz

          0 . . . .500. . . .1000. . . .1500. . . .2000. . . .2500 Hz
                                    |
                                    |

                           Center Frequency: 01360 Hz

         On a fast PC  the SPECTRUM function (F7)  can be used for  more
         precise tuning.   Adjust the  radio so  that the  CW signal  is
         centered between the green marker lines.  To start the  decoder
         select CW from the MODE menu or hit F2.

         There are two problems encountered with CW decoding in HamComm.

         Problem 1: Tone detection

         For many  people it  is obvious  that an  RTTY signal  has  two
         states, usually called mark/space or  high/low tone.  Any  data
         transmission requires at least two states  for 1 bit at a  time
         and CW is no  exception.  So  what are the  two states for  CW?
         They are the tone and ... noise !  You may be surprised to hear
         that a certain amount of noise is required by HamComm to detect
         that the tone  has ended.   For  this reason  CW decoding  with
         HamComm works not very well with narrow filters.

         HamComm has an indicator for the tone detector output.  At  the
         bottom of the RX window, just to the right of the WPM  display,
         is a  small  white  dot that  jumps  up  and down:  up  =  tone
         detected, down  = no  tone (noise)  detected.   Listen  to  the
         signal and watch the bouncing dot.  It should follow the signal
         precisely and  not  jump  around  nervously  or  stick  to  one
         position.

         The  input  signal  is  compared  to  the  currently   selected
         mark/space tones.  To be regarded  a valid tone the signal  has

                                        20



         HamComm 3.1                  Manual               June 10. 1996

         to stay in that  range for a  certain amount of  time.  So  the
         behaviour of  the detector  depends on  the currently  selected
         shift.

         The tone detector output as displayed  by the dot is the  input
         to the next stage, the character decoder.


         Problem 2: Character decoding

         In theory a  dash is three  times as long  as a  dot, the  gaps
         within  a  character  are   dot-sized  and  the  gaps   between
         characters are dash-sized.  In reality there are short and long
         tones and gaps of  variable size because  CW is usually  'hand-
         made.'   The  speed and  length  ratios also  change  during  a
         transmission if the operator gets tired or bored.

         Overall decoding quality mainly  depends on the tone  detector.
         HamComm keeps a floating average of the tone duration to adjust
         to speed changes.   If  the signal is  too noisy  the dots  and
         dashes will get  broken into many  short ones.   The  character
         decoder then gets bursts of very short tones which look like  a
         high-speed CW signal and  tries to adjust.   The WPM  indicator
         goes up and shows a much too high value resulting in  sequences
         of 'e' and 't' characters.

         Especially under noisy condition you  may get better result  if
         you turn the automatic speed adjustment  off and select the  CW
         speed manually.  Disable the AutoWPM  option on the SPEED  menu
         and select the desired speed.

         If you are not familiar with Morse code even a perfect copy may
         look  like  garbage  to  you.     CW  operators  love  to   use
         abbreviations for almost  everything:   'gn es  hpe cuagn'  for
         example means "good night and i hope to see you again".


         30 SITOR A/B

         SITOR (SImplex Teleprinting Over Radio) is a telegraphy  system
         used for  message exchange  between  ships and  land  stations.
         There are two modes called SITOR A and SITOR B.

         SITOR has been  adopted for ham  radio as  AMTOR.   Technically
         AMTOR ARQ is therefore  the same as SITOR  A, AMTOR FEC is  the
         same as SITOR B.

         See the section on AMTOR for more information.


         31 NAVTEX

         The NAVTEX system on 518kHz employs SITOR B for transmission of
         navigational and meteorological information.   AMTOR FEC  works
         like SITOR B and can thus be used to monitor NAVTEX messages.

         Please note that 518kHz is the RF frequency of the signal.   To
         hear it in USB tune to 516.6kHz.  Since there are many stations
         around the world all using the same frequency they have to  use


                                        21



         HamComm 3.1                  Manual               June 10. 1996

         a fixed time  schedule for their  transmissions.   It may  take
         quite some time until your hear a signal.

         See  the  section  on  AMTOR   for  more  information  on   FEC
         monitoring.


         32 AMTOR

         AMTOR (AMateur Teleprinting Over Radio)  is an adoption of  the
         maritime SITOR  system for  Amateur  Radio by  Peter  Martinez,
         G3PLX.  He  was the  first who  designed and  built a  low-cost
         AMTOR code converter.  AMTOR works exactly like SITOR with  the
         addition of a LISTEN mode for ARQ transmissions.

         AMTOR provides two modes of communication, ARQ and FEC.  In the
         ARQ (Automatic ReQuest) mode the 'information sending  station'
         (ISS)  transmits   a  block   of  three   characters  and   the
         'information  receiving   station'  (IRS)   replies  with   one
         character for acknowledgment.   If the  block arrived intact  a
         'positive acknowledgment' (ACK) is  sent and the ISS  continues
         with the  next block.   Otherwise  a 'negative  acknowledgment'
         (NAK) character is sent and the ISS repeats the block in error.

         Because of this handshaking  only two stations can  participate
         in an ARQ link.  Other stations can monitor the QSO, but  there
         will be no error correction.

         FEC (Forward Error  Correction) is  a broadcast  mode with  one
         sender and many receivers.  The sending station transmits  each
         character twice,  but not  in a  row.   Between the  first  and
         second transmission  four other  characters  are sent,  so  the
         second transmission is delayed by 350ms.

         Speed for ARQ and FEC transmission  is always 100 Baud (=  10ms
         per bit) and will be automatically selected by HamComm.


         33 FEC monitoring

         The procedure to monitor FEC  transmissions is very similar  to
         RTTY monitoring.  Select AMTOR FEC from the MODE menu or hit F5
         to activate FEC mode.  The speed is internally set to 100  Baud
         so you don't have  to change the Baud  setting manually.   Make
         sure that a shift of 170Hz is selected on the KEYING menu.  Set
         the keying direction to 'normal' for USB, select 'reverse' when
         receiving in LSB.  Tune in to the FEC signal in the same way as
         described for RTTY above.

         AutoUnshift should be disabled, check the  TEXT menu.  The  AFC
         feature may be helpful to  compensate receiver drift for  long-
         term reception.

         HamComm may need  a few  seconds to get  in sync  with the  FEC
         signal.   Instead  of the  Baud  indicator there  is  a  status
         display in the lower left corner.  STBY (=Standby) is displayed
         while HamComm  is  looking for  a  valid signal.  ERR  (=Error)
         indicates  that  an  illegal   character  was  received,   TRFC
         (=Traffic) indicates a valid character.


                                        22



         HamComm 3.1                  Manual               June 10. 1996



         34 FEC transmission

         To transmit  an FEC  signal just  activate  AMTOR FEC  mode  as
         described above and hit control-T or toggle RX/TX mode from the
         MODE menu.  The text to send is entered in the transmit window.
         Use  the  EOT  character  (default  =  control-backspace)   for
         automatic return to RX mode at the end of the text.


         35 ARQ LISTEN mode

         To monitor an ARQ transmission select AMTOR ARQ LISTEN from the
         MODE menu or hit F4.  The  speed is internally set to 100  Baud
         so you don't have  to change the Baud  setting manually.   Make
         sure that a shift of 170Hz is selected on the KEYING menu.  Set
         the keying direction to 'normal' for USB, select 'reverse' when
         receiving in  LSB.   AFC and  AutoUnshift should  be  disabled.
         Tune in to the ARQ signal in the same way as described for RTTY
         above.

         AMTOR ARQ sends  a block about  twice a  second (every  450ms).
         The signals  are  easily  identified  by  their  characteristic
         chirp-chirp sound.    It  requires some  practice  und  careful
         listening to  tell wether  the station  is sending  information
         blocks or acknowledgment  characters.   Information blocks  are
         about 210ms long, acknowledgments only  70ms.  This results  in
         slightly different sounds.   Of course only information  blocks
         will be decoded.  If you are not sure try to take a look at the
         signal using the SCOPE function.

         In ARQ  LISTEN mode  HamComm tries  to find  valid  information
         blocks to lock  on the incoming  signal.  Instead  of the  Baud
         indicator there is a  status display in  the lower left  corner
         indicating one of the following conditions:

         STBY    (Standby)   looking for valid information blocks
         LOCK    (Locked)    valid blocks found, locked on signal
         TRFC    (Traffic)   valid character received
         ERR     (Error)     invalid   character   received   (at   this
                             station)
         REQU    (Request)   ISS   requests   retransmission   of   last
                             acknowledgment
         REPT    (Repeat)    ISS  sends  same  block  again  (block  not
                             displayed)
         IDLE    (Idle)      ISS has no text to send


         36 ARQ transmission

         Calling cq:
         FEC is  used for  calling cq  in AMTOR.   Keying  direction  is
         'normal' in USB and 'reverse' in LSB.  Switch to FEC mode  (F5)
         and hit control-T to  start the transmitter.   Let it idle  for
         half a minute before  entering text.  The  signal of an  idling
         FEC station has a special sound that is immediately  recognized
         by experienced AMTOR operators.  It also allows other  stations
         to tune and synchronize to your signal.


                                        23



         HamComm 3.1                  Manual               June 10. 1996

         A typical cq call looks like this:

         CQ CQ CQ DE DL5YEC DL5YEC DL5YEC SELCAL DYEC DYEC DYEC

         Repeat the text four or five times, then terminate with 'PSE K'
         and go back to RX mode.  The EOT character  (control-backspace)
         can be used to automatically switch  TX mode off.  If there  is
         no reply, repeat the procedure.

         The other station can  call you back using  either FEC or  ARQ.
         If it  comes  back in  ARQ  you have  to  switch to  AMTOR  ARQ
         manually using the MODE menu or ALT-F4.  When your station  has
         received it's own SELCAL as defined  in HC31.CFG it will  start
         to reply with  acknowledgments and the  other station 'has  the
         keys'.

         In AMTOR ARQ  the character sequence  '+?' is used  by the  ISS
         (information sending station)  to turn  the link  around.   The
         change-over is done automatically, so whenever you receive  the
         magic '+?' sequence your station becomes the ISS.  Don't forget
         to terminate your  text with  the same  sequence.   Transmitted
         text will appear in the RX window in a different color.

         In ARQ there  is also  a way  to 'seize'  the link.   Just  hit
         control-T while you are the IRS (information receiving station)
         and a change-over procedure is initiated.  This feature  should
         only be used for urgent messages like 'TX IS BURNING'.

         To shut down the link use  the EOT character while you are  the
         ISS  Transmission  will also  be disrupted  immediately if  any
         other operating mode like CW, FEC or BAUDOT is selected.


         Calling an ARQ station:
         If you want  to answer a  cq call or  contact one  of the  many
         AMTOR mailboxes,  you  have  to  specify  the  SELCAL  of  that
         station.  Select item 'Define SELCALL'  from the TEXT menu  and
         enter the four-letter selective call.  Switch to AMTOR ARQ mode
         (ALT-F4) and  hit  control-T.    Your  station  will  start  to
         transmit special information  blocks containing  the SELCAL  of
         the other station.   Transmission will  stop if  there isn't  a
         reply within a minute.  If  the link is made, operation is  the
         same as described above.


         37 Error correction

         There is  no  communications  protocol that  can  guarantee  an
         error-free data transmission.   The differences  are mainly  in
         the reliability of the  error detection scheme  in use.   Newer
         modes like packet radio  and PACTOR add a  CRC checksum at  the
         end of a data block.  The probability that a transmission error
         will go by unnoticed is very low.

         With the AMTOR FEC and ARQ modes there is no checksum.  The  7-
         bit AMTOR code is basically the 5-bit Baudot code with two bits
         added to  each  character.   With  seven  bits  there  are  128
         possible combinations, but  only the  35 codes  are used  which
         have four bits high and three  bits low.  An error is  detected
         if any of the other codes is received.

                                        24



         HamComm 3.1                  Manual               June 10. 1996


         If two or  more bits get  mutilated the result  may be  another
         valid character.  AMTOR links are  not error-free,  there  will
         be an undetected transmission error every now and then on a bad
         link. This isn't really  a problem as  normally there are  more
         typos than transmission errors.


         38 Clock correction

         One reason why AMTOR ARQ is  much more robust than RTTY is  the
         synchronisation.   Once the  link is  established the  internal
         clocks are kept in  sync so both  stations know very  precisely
         when the next bit will arrive.

         The ARQ station initiating a link  is called MASTER, the  other
         station is SLAVE.  This is not to be confused with ISS and IRS.
         The SLAVE will constantly adjusts its clock to the MASTER clock
         until the link is terminated.

         The time  references  of  the  commercial  SITOR  stations  are
         accurate to about +/-30ppm (parts  per million).  When  HamComm
         was tested on many different PCs  it was found that their  xtal
         oscillators sometimes deviate up to 400ppm.

         One may ask  why the  clocks have to  be so  accurate when  the
         SLAVE has to adjust  to the MASTER  anyway.  Reception  suffers
         from noise and fading.  If the signal is bad there is not  much
         phasing information  available to  adjust  the clock,  so  both
         stations would  quickly run  out of  sync. Accurate  timing  is
         therefore essential to keep the link going, especially when the
         conditions are poor.

         So the clock  has to  be corrected.   To  find the  'clockcorr'
         value for a  specific PC, an  ARQ reference  signal is  needed.
         This could be an AMTOR station but it is usually easier with  a
         SITOR signal. If you have a receiver that can tune outside  the
         amateur bands,  try to  find a  SITOR station  around  2020kHz,
         4200kHz, 6320kHz  or 8400kHz.   We  need a  strong signal  with
         information blocks.  Select AMTOR ARQ LISTEN mode (F4) and tune
         to the signal.

         A correction counter is shown in  the lower left corner of  the
         RX window, to the right of link status display.  The correction
         counter will change as soon as HamComm is locked on the  signal
         and starts to decode.  The link status now displays TRFC, REPT,
         REQU or IDLE.  Hit the ESC  key to reset the counter and  watch
         the it.  We need  to know how many  seconds it takes until  the
         counter has  reached  the  value  10 or  -10.    If  there  are
         interruptions in the transmission you  will have to start  over
         again.  Repeat the procedure a  few times to make sure you  got
         the right value.   If it takes more  than two minutes to  reach
         the final count your PC happens to be accurate enough.

         The clockcorr value is the number of seconds times 100.  If the
         count is negative  then the  clockcorr value  is also  negative
         Example: The counter reached -10 in 43 seconds.  The  clockcorr
         value is therefore -4300



                                        25



         HamComm 3.1                  Manual               June 10. 1996

         The clockcorr setting  has to be  changed in the  configuration
         file HC31.CFG.  Using your favourite editor, find the line "set
         clockcorr 0"  and change  it to  the value  calculated  before.
         With the right value the correction count will be stable during
         ARQ reception.


         39 Macro keys

         A macro  key  can  be used  to  replay  a  previously  recorded
         sequence of  keystrokes.   The digits  on the  top row  of  the
         keyboard are used as macro keys while the ALT key is depressed.
         They are normally located  right above the  QWERTY... row.   Do
         not confuse these keys with the numeric keypad!

         In the beginning there are no keystrokes assigned to the  macro
         keys, so pressing ALT-1, ALT-2...ALT-9 or ALT-0 has no  effect.
         To start recording, select item 'Macro recorder' from the  FILE
         menu.  A message box will appear confirming that recording  has
         been started.  When the ENTER key is hit, the message box  will
         go away and from now on  up to 250 keystrokes will be  recorded
         along with  normal  processing.    A  blinking  "! RECORDING !"
         message is shown  at the lower  right corner of  the screen  to
         remind you that the recorder is still active.

         Now hit one of the macro  keys to stop recording and to  assign
         the keystroke sequence  to that key.   This  also replaces  any
         previous assignment.  A message box will appear to confirm that
         macro recording has terminated.   Every time  the macro key  is
         hit the recorded keystroke sequence will be replayed just  like
         it had been typed again.

         To terminate  recording without  changing  any macro  key  just
         select 'Macro recorder' again  from the FILE  menu.  A  message
         box will  appear  to  confirm that  macro  recording  has  been
         canceled.

         To clear  a macro  key start  recording in  the usual  way  and
         directly after that hit the key to be cleared.  This will erase
         any previous recording  assigned to that  macro key.   Again  a
         message box will confirm the result.


         40 SHIP/SYNOP decoder

         Weather reports are transmitted by many stations troughout  the
         world, 24 hours  a day.   If  you live  in europe  try to  copy
         Quickborn Meteo  (near  Hamburg,  Germany) on  4583,  7646  and
         11638kHz, or Bracknell (UK) around  4488kHz.  In north  america
         try CFH (Halifax,  Nova Scotia) on  4271, 6496.5 and  10536kHz.
         There are many others between 4000 and 5000kHz.   Transmissions
         are normally in Baudot, 425Hz shift, 50 or 75 Baud.

         The SYNOP format is used for  reports from land stations,  SHIP
         format is  used  for  reports from  ships  and  other  maritime
         vessels.   The messages  include data  about temperature,  wind
         speed/direction,   cloud   cover,   precipitation,   dew-point,
         pressure and other  meteorological information.   SHIP  reports
         also include the current position of the vessel.


                                        26



         HamComm 3.1                  Manual               June 10. 1996

         Land stations are  identified by a  five-digit station  number.
         These are fixed stations, so their geographical position is not
         transmitted with a  SYNOP report.   To give you  a better  idea
         where the reporting  station is located,  HamComm comes with  a
         list  of  about   10000  station  numbers,   their  names   and
         geographical positions.   The program  will automatically  pick
         the correct entry from this list while decoding a SYNOP report.

         A typical undecoded message looks like this:

         zczc 548
         sien42 edzw 141500
         aaxx 14154
         01465 42889 42715 10084 20022 40159 52033 81048=
         02060 41480 40000 11088 21113 40060 52035 72272
         83530 333 83694=
         nnnn

         This is what you get if the SHIP/SYNOP decoder is switched off.

         The first line of a message starts with zczc and a  three-digit
         transmission sequence  number.   The second  line is  a  header
         describing the following information.  Here 'sien42'  indicates
         a "synoptic report at intermediate hours" for northern  europe,
         'edzw' is the international  four-letter location indicator  of
         the station originating or compiling the bulletin and  '141500'
         means 3pm UTC on day  14 of the current  month.  'aaxx' is  the
         indicator for SYNOP reports, 'nnnn' marks the end of a message.

         There  are  other  formats  in  use  for  different  kinds   of
         information.  Currently HamComm only supports decoding of  SHIP
         and SYNOP reports.  A message  may contain one or more  reports
         separated by = characters.  Explaining the reports in detail is
         beyond the scope of this manual.

         With the WX decoder switched on  (from the TEXT menu) the  same
         message looks like this:

         zczc [start] 548 [message 548]
         sien42 [Synoptic reports at intermediate hours (SYNOP, SHIP)]
          [Northern Europe]
          edzw [Offenbach (MET/COM Centre)]
          141500 [day:14 UTC:1500]
         aaxx [SYNOP]
          14154 [day:14 UTC:1500]
                [Wind speed obtained from anemometer (knots)]

         01465 [Norway, 58024'N 008048'E TORUNGEN (LGT-H)]
          42889 [manned] [cloud height:2000-2500m] [visibility:75km]
          42715 [cloud cover:4/8] [wind dir:270 deg, speed:15]
          10084 [air temp:+8.4]
          20022 [dew-point temp:+2.2]
          40159 [pressure at sea level:1015.9hPa]
          52033 [pressure:increasing] [change in 3h:3.3hPa]
          81048 [cloud info]

         =
         02060 [Sweden, 68041'N 021032'E NAIMAKKA]
          41480 [manned] [cloud height:300-600m] [visibility:30km]
          40000 [cloud cover:4/8] [wind dir:calm, speed:0]

                                        27



         HamComm 3.1                  Manual               June 10. 1996

          11088 [air temp:-8.8]
          21113 [dew-point temp:-11.3]
          40060 [pressure at sea level:1006.0hPa]
          52035 [pressure:increasing] [change in 3h:3.5hPa]
          72272 [past wx: snow, or rain & snow mixed,
                          cloud cover > 1/2 of sky]
                [wx now: Snow]
          83530 [cloud info]
          333 [section 3]
          83694 [clouds:3/8, stratocumulus, 1000-1500m]

         nnnn [EOM]

         HamComm displays  the  incoming text  just  as before.  The  WX
         decoder watches  the  characters  go by,  waiting  for  certain
         keywords like zczc  (start of msg),  aaxx (SYNOP report),  bbxx
         (SHIP report)  and nnnn  (end of  msg) to  synchronize with  an
         incoming message.   If  it thinks  it knows  what the  text  is
         about,  it  starts  to  insert  comments.    The  comments  are
         surrounded   by   square   brackets   and   therefore    easily
         distinguished  from  the  normal  text  (there  are  no  square
         brackets in the Baudot character set).

         There are other ways to build  a SHIP/SYNOP decoder.  It  could
         collect all data for a report and then display the result in  a
         nicely formatted way  However, there is a problem.  The kind of
         RTTY  transmission  used  for   these  reports  has  no   error
         correction,  not   even  error   detection.     It's  hard   to
         automatically classify  a  message  as  ok  or  garbled.    For
         example: if the program says there  are +30 degrees celsius  in
         Greenland and it's december, you  will hopefully not buy  that.
         HamComm has no  idea where Greenland  is and  not the  foggiest
         about the climate there, so it can't catch that type of error.

         The program displays the incoming text as received, so you  can
         see if there is garbage coming in.  Usually it is quite obvious
         if the input is bad.  With  a WX decoder working like a  'black
         box' it  is sometimes  very hard  to  see how  it came  to  its
         conclusions and what to believe or not.


         41 Scope function

         In RX  mode the  tone decoder  routine calculates  the  current
         signal frequency for use  by other parts of  the program.   The
         SCOPE function uses this value to display a graph of the  input
         frequency vs. time.  This is the blue line on the SCOPE screen.

         The tone decoder also  maintains a floating average  frequency.
         The effect is very similar to a low-pass filter and is used for
         noise reduction.   The result is  displayed at the  top of  the
         screen as a red line.

         The solid  green  line  marks  the  currently  selected  center
         frequency and the dotted  lines above and  below show the  mark
         and space tones.  For RTTY reception the center line should  be
         in the  middle  between the  mark  and  space tones.    For  CW
         reception the signal  should match the  center frequency.   All
         signals outside  the  area  marked  by  the  dotted  lines  are
         ignored.

                                        28



         HamComm 3.1                  Manual               June 10. 1996


         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                      '+'  toggle display of decoded signal
                      '*'  toggle grid display
                      'B'  toggle position of red line
                     HOME  reset sample rate to 1ms
                    PG-UP  sample rate faster
                  PG-DOWN  sample rate slower
                    ENTER  hold display immediately
                    SPACE  return to RX/TX screen

         The right mouse  button holds  the display  at the  end of  the
         current sweep.  The  left mouse button  activates the menu  bar
         just like F10.

         The  red  line  (input  signal  after  low-pass)  is   normally
         displayed at the top  of the screen to  not interfere with  the
         blue line.   In its second  position it will  overlay the  blue
         line to compare the two signals.

         Display of the decoded signal is normally disabled.  It can  be
         found at  the bottom  of the  screen and  shows the  mark/space
         states for RTTY and tone/no-tone states for CW reception.

         With some practice it is quite easy to determine the signal you
         are listening to by watching the SCOPE display.  CW, AMTOR  ARQ
         and FEC,  Packet  Radio  and  RTTY  show  their  characteristic
         patterns and you can also  watch unstable VFOs sweeping  slowly
         across the band.


         42 Spectrum function

         On entry to the Spectrum function a graphics mode according  to
         the video card and monitor in use is activated.

         Every millisecond the current input frequency is checked.   For
         every frequency there is a counter and the one that corresponds
         to the current  frequency is incremented.   All counter  values
         are displayed as vertical  lines with each  sweep from left  to
         right  The higher the count, the longer the line.  What you see
         on the screen is therefore not the true audio spectrum but  the
         result at the output of the tone decoder routine.  An opamp and
         a few lines of code can't substitute a real spectrum analyzer.

         When set to 1Hz per pixel  SPECTRUM has the best resolution  of
         all display functions.  For example,  the actual shift used  by
         an RTTY station can be determined quite accurately.










                                        29



         HamComm 3.1                  Manual               June 10. 1996

         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                      '-'  toggle raw/filtered data
                      '+'  toggle 'shaddow' (color displays only)
                      '*'  toggle dot/line mode
                     HOME  reset, start at 200Hz, 3Hz per pixel
                    PG-UP  zoom in
                  PG-DOWN  zoom out
                     LEFT  lower frequencies
                    RIGHT  higher frequencies
                    ENTER  hold display
                    SPACE  return to RX/TX screen

         The right mouse  button holds  the display  at the  end of  the
         current sweep.  The  left mouse button  activates the menu  bar
         just like  F10.   If you  have a  slow PC  then don't  use  the
         SPECTRUM function,  you might  get  frustrated.   There  simply
         isn't enough CPU power to keep the display in motion.  AT class
         maschines and real fast XTs should be ok.

         The SPECTRUM function has been found to be quite  entertaining,
         especially with a color display.  Next time you got visitors in
         your shack  who don't  know what's  going  on just  start  this
         function, turn the lights low and tune across a crowded band.


         43 Bitlength statistics

         The BITLENGTH function is  a graphics display  of the MARK  and
         SPACE pulse length as detected by  HamComm.  It's main  purpose
         is to quickly get an idea about the speed of the signal.

         With every transition of the  decoded MARK/SPACE signal a  high
         or low  pulse  ends.   The  upper  histogram  shows  the  pulse
         duration statistics  of the  high pulses,  the lower  histogram
         shows the statistics of the low pulses.

         Before using this function the center frequency must be set  to
         the center  between the  MARK and  SPACE tones,  otherwise  the
         pulse width display will suffer from distortion.

         The shortest pulses of an RTTY signal are normally equal to the
         length of one bit.  Therefore  the leftmost peak indicates  the
         Baud of the incoming signal.   A noisy signal produces lots  of
         short spikes.  They tend to  accumulate at the left end of  the
         histogram and should be ignored for Baud analysis.

         The BITLENGTH  function tries  to identify  the leftmost  valid
         peek automatically,  but  this  may fail  with  noisy  signals.
         Below each histogram the Baud corresponding to the highest peak
         is displayed.  There is also a MARKER that can be moved  freely
         using the LEFT and RIGHT keys.







                                        30



         HamComm 3.1                  Manual               June 10. 1996

         The display can be controlled with the following keys:

                       F1  display help screen
                      F10  activate menu bar
                    PG-UP  zoom in
                  PG-DOWN  zoom out
               LEFT,RIGHT  move marker
             CONTROL-LEFT  move marker, fast mode
            CONTROL-RIGHT   "     "      "    "
                    ENTER  hold display
                    SPACE  return to RX/TX screen

         The marker can  also be controlled  by moving  the mouse  while
         holding  down  the  right  mouse  button.    The  Baud   number
         corresponding to the marker position is displayed at the  upper
         left corner of the screen.

         The left mouse button activates the menu bar just like F10.


         44 Interface checkout

         So you  have  build  the  interface  and  made  the  neccessary
         connections to the radio.  You fire up the program and you  see
         - nothing.

         To find out what is going wrong let's start at the serial  port
         HamComm needs to know two parameters about a COM port:

         1. the port address
         2. the IRQ number

         The  port  address  and  IRQ  number  for  COM1  and  COM2  are
         standardized  and  therefore  predefined  in  HC31.CFG  to  the
         following values:

                     addr   IRQ
              COM1   3F8h    4
              COM2   2F8h    3

         For other serial ports there is  no real standard, so COM3  and
         COM4 are not defined in the supplied HC31.CFG.  Undefined ports
         can not be selected from the PORT menu.


         45 Port address

         Start the  program and  select entry  'HamComm' from  the  INFO
         menu.  A small window  appears displaying, among other  things,
         the port address  and IRQ  of the  serial ports  as defined  in
         HC31.CFG.  If  the values for  the port you  want to use  don't
         match the hardware, correct HC31.CFG with a text editor.

         Remove the interface for now.  Select the correct port from the
         port menu, then hit F3 to  activate the RX/TX screen.  Using  a
         voltmeter check the RTS and DTR outputs of the serial port with
         respect to the GND pin.  RTS should have a negative voltage and
         DTR should be positive.



                                        31



         HamComm 3.1                  Manual               June 10. 1996

         Now switch to transmit  (TX) mode.  This  can be done from  the
         MODE menu but it's easier to hit control-T.  When switching  to
         TX mode both RTS and DTR reverse their polarity, so RTS  should
         now be positive and DTR should be negative.

         If they don't, here is a list of what might be wrong:

          - the voltmeter is broken.

          - you are measuring at the wrong socket.
            The serial ports of a PC are normally
            25-pin or 9-pin male SUB-D sockets.

          - you are measuring at the wrong pins.

                      4     7                              4   5
                     RTS   GND                            DTR GND
            ----1-----|-----|-----------13---     ----1-----|-|----
            \         |     |               /     \         | |   /
             \  o o o o o o o o o o o o o  /       \  o o o o o  /
              \  o o o o o o o o o o o o  /         \  o o o o  /
               \             |           /           \   |     /
                14-----------|---------25             \6-|---9/
                            DTR                         RTS
                             20                          7


          - you have selected the wrong com port. Check the PORT menu.

          - the port address as defined in HC31.CFG for this port is not
            correct.  Check the INFO menu and HC31.CFG.

          - the com port has a different address from what you think.
            The address can often be selected with jumpers on the
            serial card.  Check the documentation for your computer.
            On some newer PCs and notebooks the com port address can
            be changed or the port can be disabled with a setup
            program.

          - if only one of the signals (RTS or DTR) changes polarity,
            the line driver for the other signal may be broken.


         46 Op-Amp power supply

         Now let's take a look at the interface.  By far the most common
         problems are:
          - wrong or missing connections
          - solder bridges and cold solder joints

         If you think the  problem is with the  interface take the  time
         and carefully inspect it under a magnifying glass.

         If that doesn't work, proceed as follows.

         Switch off the computer and connect the interface to the serial
         port. Don't  connect it  to the  radio yet,  connect the  audio
         input to  GND. If  possible the  interface should  be  directly
         plugged to  the com  port. Any  cable between  the PC  and  the
         interface should be avoided, it may degrade the signal quality.

                                        32



         HamComm 3.1                  Manual               June 10. 1996


         Switch the PC on, start HamComm, select the right port from the
         PORT menu and hit F3 for the RX/TX screen.  Check that RTS  and
         DTR still change  polarity when you  toggle between  RX and  TX
         mode.

         Check the supply voltages  at the op-amp  with respect to  GND.
         The positive voltage  at pin  7 should  be +5V  or higher,  the
         voltage at pin 4 should be -5V or lower (more negative).

                         +V out
                       8  7  6  5
                       |  |  |  |    Operational Amplifier
                     |------------|
                     |            |  LM741 or TL071
                     |            |
                     |-|          |  DIL-8 package, top view
                       |          |
                     |-|          |   +V = positive supply
                     |            |   -V = negative supply
                     |            |   -I = inverting input
                     |------------|   +I = non-inverting input
                       |  |  |  |    out = output
                   Pin 1  2  3  4
                         -I +I -V

         Check the voltages both in RX and TX mode at the op-amp.   Here
         they should  NOT  change  polarity, otherwise  the  IC  may  be
         permanently damaged.   If  they do  or if  the readings  change
         significantly in RX and TX mode, check the wiring and  polarity
         of the four diodes between the  PC and the op-amp.  Also  check
         the two capacitors used for buffering the supply.

         Although only a current of a few milliamperes is needed for the
         op-amp, some  com ports  can not  deliver the  required  supply
         voltages.   You may  try  to find  an  op-amp that  draws  less
         current  but  the  easiest  solution  is  to  use  two   9-Volt
         batteries:

                                 bat 1      bat 2

                                  ||         ||
                 op-amp pin 7 <---||----O----||---> op-amp pin 4
                                 +||-   |   +||-
                                       GND

         If the power supply is ok  we will now try  to find out if  the
         op-amp works  correctly.    First  check  the  voltage  at  the
         inverting and non-inverting inputs.  Both should read 0 or VERY
         close to 0 volts with respect to GND.  If they don't, there  is
         probably a wiring error or the chip is broken.

         Temporarily connect a  resistor of about  1M (megaohm)  between
         the non-inverting input  (pin 3) and  the positive supply  (pin
         7).   Be very  careful not  to short  any pins.   The  op-amp's
         output should go as high as it can go, which is normally  about
         1 volt below the positive supply.

         Remove the resistor and  connect it between  the input (pin  3)
         and the negative supply (pin 4).   The output should now be  as

                                        33



         HamComm 3.1                  Manual               June 10. 1996

         low as it can go, about  1 volt above (more positive) than  the
         negative supply.

         Check the output signal directly at the DSR pin of the com port
         to make sure that the wiring is ok.  This is only a very simple
         test wich the op-amp will only fail if it is badly damaged.

         The output  of  the op-amp  will  also be  positve  or  negativ
         without the resistor. This is normal and doesn't mean that  the
         chip is broken.


         47 IRQ number

         Now connect the input of the  interface to the audio output  of
         the receiver.  The  op-amp is quite  sensitive and should  work
         even with very low  signals.  Some radios  have a socket for  a
         tape recorder where the amplitude is independent of the  volume
         setting.  Try that first.

         Tune in to some strong signal,  preferably to a constant  tone.
         At the DSR pin  of the com  port there should  now be a  square
         wave signal.  The amplitude at DSR should have at least the +/-
         5V swing required to reliably drive an RS-232C input.

         Start  HamComm  to  check  if  the  signal  at  DSR   generates
         interrupts.  Select the right port  from the PORT menu and  try
         the TUNE, SCOPE or SPECTRUM function from the MODE menu.

         If all of these functions seem to be dead, HamComm doesn't  get
         any hardware interrupts  from the  serial port.   Select  entry
         'HamComm' from the INFO menu and check the displayed IRQ number
         for the port you want to use.  If it's wrong, specify the right
         one in HC31.CFG.

         Make sure that the port really uses the IRQ you think it  does.
         Many serial cards have jumpers or  small switches for IRQ  line
         selection.  Some  newer PCs and  notebooks can do  this from  a
         setup program.

         Please note, that an IRQ line can only be used by one device at
         a time.  For example, if  you have a mouse  on IRQ 4 you  can't
         use a COM port on the same IRQ at the same time.


















                                        34



         HamComm 3.1                  Manual               June 10. 1996


         48 Appendix A - Key assignment summary

         --- All Windows ---

         F1                  display help text
         F2                  RX/TX window, CW mode
         ALT-F2              RX/TX window, ASCII mode, 7 bit
         F3                  RX/TX window, Baudot mode
         ALT-F3              RX/TX window, ASCII mode, 7 bit
         F4                  RX/TX window, AMTOR ARQ Listen
         ALT-F4              RX/TX window, AMTOR ARQ mode
         F5                  RX/TX window, AMTOR FEC mode
         F6                  Bitlength display
         F7                  Spectrum display
         F8                  Scope display
         F9                  Tune window
         F10                 Menu bar

         ALT-1               execute macro 1
         ALT-2               execute macro 2
         ALT-3               execute macro 3
         ALT-4               execute macro 4
         ALT-5               execute macro 5
         ALT-6               execute macro 6
         ALT-7               execute macro 7
         ALT-8               execute macro 8
         ALT-9               execute macro 9
         ALT-0               execute macro 0

         ALT-F5              WX decoder off
         ALT-F6              WX decoder on
         ALT-F7              AFC off
         ALT-F8              AFC on
         ALT-F9              external converter off
         ALT-F10             external converter on

         ALT-C               Callsign decoder
         ALT-X               Terminate programm


         --- TUNE Window ---

         HOME                reset center frequency
         LEFT                decrease center frequency
         RIGHT               increase center frequency
         SPACE               return to RX/TX screen


         --- RX/TX Window ---

         SHIFT-F1            Standardtext 1
         SHIFT-F2            Standardtext 2
         SHIFT-F3            Standardtext 3
         SHIFT-F4            Standardtext 4
         SHIFT-F5            Standardtext 5
         SHIFT-F6            Standardtext 6
         SHIFT-F7            Standardtext 7
         SHIFT-F8            Standardtext 8
         SHIFT-F9            Standardtext 9

                                        35



         HamComm 3.1                  Manual               June 10. 1996

         SHIFT-F10           Standardtext 10

         LEFT                move TX cursor left, 1 character
         RIGHT               move TX cursor right, 1 character
         UP                  move TX cursor up, 1 line
         PAGE-UP             move TX cursor up, 1 page
         DOWN                move TX cursor down, 1 line
         PAGE-DOWN           move TX cursor down, 1 page
         HOME                move TX cursor to first line
         END                 move TX cursor to last line
         INSERT              toggle insert mode on/off
         DELETE              delete character under cursor
         BACKSPACE           delete character left to cursor
         TAB                 toggle NORMAL/REVERSE keying direction
         ENTER               transfer text line to transmit buffer

         CONTROL-A           move TX cursor to beginning of line
         CONTROL-B           AMTOR details on/off
         CONTROL-D           insert time and date
         CONTROL-E           move TX cursor to end of line
         CONTROL-F           open/close logfile
         CONTROL-H           same as BACKSPACE
         CONTROL-I           same as TAB
         CONTROL-L           toggle AutoUnshift on/off
         CONTROL-M           same as ENTER
         CONTROL-P           toggle transmit monitoring on/off
         CONTROL-S           send textfile
         CONTROL-T           toggle transmit/receive mode
         CONTROL-W           toggle Line/Word mode
         CONTROL-X           clear TX window line
         CONTROL-Z           insert time

         CONTROL-LEFT        roll RX window backwards, 1 line
         CONTROL-HOME        roll RX window backwards, 1 page
         CONTROL-RIGHT       roll RX window forewards, 1 line
         CONTROL-END         roll RX window forewards, 1 page
         CONTROL-PAGE-UP     resize RX/TX window
         CONTROL-PAGE-DOWN   "      "     "

         --- SCOPE Display ---

         '+'                 toggle display of decoded signal
         '*'                 toggle grid display
         'B'                 toggle position of red line
         HOME                reset sample rate
         PAGE-UP             sample rate faster
         PAGE-DOWN           sample rate slower
         ENTER               hold display immediately
         SPACE               return to RX/TX screen












                                        36



         HamComm 3.1                  Manual               June 10. 1996

         --- SPECTRUM Display ---

         '-'                 toggle raw/filtered data
         '+'                 toggle 'shaddow' (color displays only)
         '*'                 toggle dot/line mode
         HOME                reset, start at 200Hz, 4Hz per pixel
         PAGE-UP             zoom in
         PAGE-DOWN           zoom out
         LEFT                lower frequencies
         RIGHT               higher frequencies
         ESC                 clear display
         ENTER               hold display
         SPACE               return to RX/TX screen

         --- BITLENGTH Display ---

         PAGE-UP             zoom in
         PAGE-DOWN           zoom out
         LEFT                move marker left
         RIGHT               move marker right
         CONTROL-LEFT        move marker left, fast mode
         CONTROL-RIGHT       move marker right, fast mode
         ENTER               hold display
         SPACE               return to RX/TX screen





































                                        37



         HamComm 3.1                  Manual               June 10. 1996


         49 Appendix B - Baudot code table


                 -- Standard --      ---- Extended ----
         Code    Upper   Figures     Lower   Punctuation

         03      A       -           a       _
         25      B       ?           b       n.a.
         14      C       :           c       ;
         09      D       WRU         d       n.a.
         01      E       3           e       n.a.
         13      F       %           f       `
         26      G       @           g       }
         20      H       #           h       {
         06      I       8           i       n.a.
         11      J       *           j       n.a.
         15      K       (           k       [
         18      L       )           l       ]
         28      M       .           m       >
         12      N       ,           n       <
         24      O       9           o       ~
         22      P       0           p       n.a.
         23      Q       1           q       !
         10      R       4           r       $
         05      S       '           s       "
         16      T       5           t       n.a.
         07      U       7           u       &
         30      V       =           v       |
         19      W       2           w       n.a.
         29      X       /           x       \
         21      Y       6           y       ^
         17      Z       +           z       n.a.

         04      SPC     SPC         SPC     SPC
         08      CR      CR          CR      CR
         02      LF      LF          LF      LF
         31      LET     LET         LET     LET
         27      FIG     FIG         FIG     FIG
         00      NIL     NIL         NIL     NIL

           CR    Carriage Return
           LF    Line Feed
          LET    Select letters
          FIG    Select figures
          SPC    Space
          NIL    Select upper/lower, fig./punct.














                                        38



         HamComm 3.1                  Manual               June 10. 1996


         50 Appendix C - Interface schematics

                                                                RS-232C
         Receive Circuit                                         25  9
                                                                pin pin
                        IC1 TL071                   D1
                         or LM741 -------*--------*-I<--*--< DTR 20  4
                                  |      |        | D2  |
                             3 |\ |      |      ---->I---
             >------||---*-----|+\ 7     |      | |
                    C1   |     |  \______|______|_|________> DSR  6  6
                  0.1uF  |   2 |  /6     |      | | D3
                         |  ---|-/       |      | --I<--
           Signal        |  |  |/ |4     |      |   D4  |
           from          /  /     ---*---|------*--->I--*--< RTS  4  7
           Receiver    R1\  \R2      |   |
                     100K/  /100K    |   | +
                         \  \       === === C2,C3
                         |  |       === === 10uF
                         |  |      + |   |  16V
             >-----------*--*--------*---*-----------------> GND  7  5

         Transmit Audio Circuit
         (omit for receive-only)  R4       R5         R6
                                  15K      15K        10K
                      --------*--/\/\--*--/\/\--*-*--/\/\--< TxD  2  3
              C4      |       |        |        | |
             0.1 uF   / R3    |        |      D5| |D6
         <----| |---->\ 10K  === C5   === C6    - v
          MIC         / var. ===.022  ===.022   ^ -
          Socket      |       |  uf    |  uF    | |
         <------------*-------*---*----*--------*-*--------> GND  7  5


         PTT Circuit
                                  C      (omit for receive-only)
         PTT <-------------------\
                           Q1     \I B       R7     D7
                           2N2222  I--------/\/\----I<-----< RTS  4  7
                                  /I         1K
                                 v
                                 | E
             <-------------------*-------------------------> GND  7  5

















                                        39



         HamComm 3.1                  Manual               June 10. 1996



         FSK Circuit
                                         (omit for receive-only)
                                  C      (optional for transmit)
         FSK <-------------------\
                           Q2     \I B       R8     D8
                           2N2222  I--------/\/\----I<-----< DTR 20  4
                                  /I         1K
                                 v
                                 | E
             <-------------------*-------------------------> GND  7  5


         D1-D8 = 1N914 or 1N4148














































                                        40



         HamComm 3.1                  Manual               June 10. 1996


         51 Appendix D - Interface supplier

         Ready-to-run HamComm-Interfaces  can  be  ordered  from  Dieter
         Dippel, DF4RD.    They  are build  with  SMD  (Surface-Mounted-
         Device) components and  housed in a  case similar  to a  mouse-
         adapter.  There are two versions available for 9-pin or  25-pin
         COM ports.

                          __                   __                 __
                        _|  |_________________|  |_
                       | |                       | |
            COM-Port   | |      SMD-HamComm      | |   RX/TX      app.
          9-pin female | |       Interface       | | 9-pin male   35mm
                       |_|   _________________   |_|
                         |__|                 |__|                __

                         |       app. 60mm       |


                          __                                      __
                        _|  |_____
                       | |         \
                       | |           \          __
                       | |             \_______|  |_
                       | |                        | |
            COM-Port   | |      SMD-HamComm       | |   RX/TX     app.
         25-pin female | |       Interface        | | 9-pin male  55mm
                       | |               ______   |_|
                       | |             /       |__|
                       | |           /
                       |_|   _____ /              |
                         |__|                     |                __
                                                  |
                         |       app. 60mm        |

         The interface also works with SSTVFAX, PKTMON, EASYFAX and  the
         well-known  JVFAX  fax/sstv  program  by  Eberhard  Backeshoff,
         DK8JV.

         For more information please request  an updated price list  and
         terms of delivery from

             Dieter Dippel, DF4RD
             Fenitzerstr. 33
             D-90489 Nuernberg
             Phone/Fax: (0) 911 / 55 92 96  between
             Mo. - Fr. 18:00 and 20:00 german local time
                    or 17:00 and 19:00 UTC












                                        41



         HamComm 3.1                  Manual               June 10. 1996



         52 Index



         A                                 F

         AAB .......................13     F1 .........................7
         AFC .......................12     FEC .......................10
         AFSK ......................17     FEC monitoring ............22
         AFSK output ...............17     FEC transmission ..........23
         AMTOR .....................22     File menu ..................7
         AMTOR ARQ .................10     Floppy .....................5
         AMTOR FEC .................10     Function keys ..............7
         AMTOR Listen mode .........10
         ARQ .......................10     H
         ARQ LISTEN mode ...........23
         ARQ transmission ..........23     Harddisk ...................5
         ASCII mode ................10     HC31.CFG ...............6; 15
         AutoUnshift ...............13     Help system ................7
         AutoWPM ...............11; 21
                                           I
         B
                                           Info menu .................15
         Baud selection ............11     Installation ...............5
         Baudot .....................9     Interface .................31
         Bit Length display ........11     Interface schematics ......16
         Bitlength statistics ......30     Introduction ...............4
         Blank lines ...............13     IRQ .......................34

         C                                 K

         Callsign decoder ..........15     Keying menu ...............12
         CGA ........................5
         Character mode ............14     L
         Clear TX buffer ...........12
         Clock correction ..........25     Laptop .....................6
         ClockCorr .................15     LCD ........................6
         COM port selection ........12     License ....................4
         Config files ...............9     Line mode .................14
         Converter, external .......17     Locator ...................15
         CW .................9; 18; 19     Logfile .................7; 8
                                           logrxlabel .................8
         D                                 logtxlabel .................8

         Define text ...............13     M
         Desqview ...................5
         Diddle ....................12     Macro files ................8
                                           Macro keys ................26
         E                                 Macro recorder .............8
                                           Menu bar ...................7
         EGA ........................6     Mode menu ..................9
         Error correction ..........24     Morse code .............9; 19
         ESC ........................7     Morse decoding ............20
         Exclusion of warranty ......5     Mouse ......................6
         Extended Baudot ...........14     Multitasking ...............5
         External AFSK .............17
         External converter ....12; 17


                                        42



         HamComm 3.1                  Manual               June 10. 1996

         N                                 Shift setting .............12
                                           SHIP/SYNOP ............15; 26
         NAVTEX ....................21     Signal decoding ...........18
         Normal ....................12     SITOR A/B .................21
                                           Speaker ...............12; 17
         O                                 Spectrum display ..........11
                                           Spectrum function .........29
         Operational Amplifier .....16     Speed menu ................11
         Options menu ..............15     Startup ....................6
         OS/2 .......................5     SuperVGA ...................6
                                           System requirements ........5
         P
                                           T
         Pactor Listen mode ........10
         Port address ..............31     Text menu .................13
         Port menu .................12     Transmit circuit ..........17
         Printer ....................8     Tune display ..............11
         PRN device .................8     TX buffer .................14
         PTT circuit ...............16
                                           U
         Q
                                           Update .....................4
         QSO count .................13
                                           V
         R
                                           VGA ........................6
         Receive circuit ...........16     Video adapter ..............5
         Reverse ...................12
         RTTY ......................18     W
         RTTY Basics ...............18
         RTTY decoding .............19     Windows ....................5
                                           Word mode .................14
         S                                 WPM selection .............11
                                           WX decoder ................14
         Scope display .............11
         Scope function ............28     X
         Screen layout ..............7
         Selection ..................7     XT .........................5
         Send text .................13
         Send text file .............9





















                                        43