TUGAS V

Tugas : Karakteristik I-V dan Frekuensi Tinggi Transistor Bipolar

___________

Title	NPN power transistor

$ Grid of the structure and doping distribution

$ SILVACO International 1991

mesh	rect	nx=31	ny=31	smooth=1

diag.flip	outf=nmesh14

x.m	n=1	l=0.0	r=1.0

x.m	n=31	l=300.0	r=1.0

y.m	n=1	l=0.0	r=1.0

y.m	n=31	l=90.0	r=1.0

$ Electrodes #1 –emitter; #2 –base; #3 –collector

region	num=1	iy.l=1	iy.h=31	ix.l=1	ix.h=31 silicon

elec	num=1	ix.l=1	ix.h=8	iy.l=1	iy.h=1

elec	num=2	ix.l=28	ix.h=31	iy.l=1	iy.h=1

elec	num=3	ix.l=1	ix.h=31	iy.l=31	iy.h=31

$ Impurity profile

doping	uniform  conc=1.0e15 n.type

doping	gauss 	conc=1e17 p.type junct=25.0

doping	gauss	conc=5.0e19 n.type junc=10.0 x.r=85.0 ratio=0.75

$

plot.1d	dop x.s=0.0 x.e=300.0 y.s=0.0 y.e=0.0 abs log points pa

plot.1d	dop x.s=0.0 x.e=300.0 y.s=0.0 y.e=90.0 abs log points pa

plot.2d	grid boundry no.top no.fill pa

plot.2d	junction boundry l.elect=1 l.bound=3.1 l.junction=6

+	no.fill pa

end

Title	NPN power transistor

$Solution with 18.0 V applied to collector

$ SILVACO International 1991

mesh 	inf-nmesh14

mater	region=1 taup0=3.5e-1 taun0=1.1e-6

models	srh auger conmob fldmob

$solve initial condition with zero carriers

symb	gummel carr=0

method	iccg	damped

solve	init

solve 	v3=18 local

$ then redo with 2 carriers

symb	newton carr=2

method	xnorm autonr

solve	v3=18 outf=transis2

end

Title 	NPN power transistor

$ Forward characteristic simulation

$ SILVACO International 1991

mesh	inf=nmesh14

mater	region=1 taup0=3.5e-7 taun0=1.1e-6

models	srh auger conmob fldmob

load 	inf=transis2

log	outf=trans21

symb	newton	carr=2

method	xnorm	autonr

solve	v3=18	v2=0.1

solve	previous	 v2=0.2 vstep=0.1 nstep=5 electr=2

solve	previous v2=0.8 outf=solvtr21

solve	previous v2=0.9 outf=soltr22

solve	previous v2=1.0 outf=soltr23

end

Title 	NPN power transistor IV plot

$ plot forward characteristic

$ SILVACO International 1991

mesh 	inf=nmesh14

plot.1d	inf=trans21 x.ax=v2 y.ax=i3 x.label=VBE y.label=IB_and_IC

+	y.log min.value=-11 x.min=0.4 points abs pa

plot.1d	inf=trans21 x.ax=v2 y.ax=i2 y.log xmin=0.4 point unch pa

plot.1d	inf=trans21 x.ax=i3 x.log y.ax=i3/i2 abs

+	y.label=”Gain” x.label=”log10(IC)”

end

Title transistor NPN

$ Karakteristik frekuensi tinggi transistor

mesh 	inf=mesh14

mater	regoin=1	taup0=3.5e-7  taun01.1e-6

model 	srh auger conmob fldmob

load	inf=solvtr21

log	aclfile=acnpn

symb	newton carr=2

method	xnorm autonr

solve	ac fre=1 fstep=4 mult.f nfstep=11 vss=5

+	max.inner=250 s.omega=0.30 terminal=2

end

Title plot frekuensi transistor NPN

$ plot Ic terhadap frekuensi

mesh	inf=nmesh14

plot.1d	inf=acnpn x.ax=freq x.log x.min=0.0 y.lab=Ic y.ax=i3 abs pa

plot.1d	inf=acnpn x.ax=freq x.log x.min=0.0 y.lab=Ic y.ax=i3 points unch pa

end

Title plot frekuensi transistor npn

$ plot ib terhadap frekuensi

mesh	inf=nmesh14

plot.1d	inf=acnpn x.ax=freq x.log x.min=0.0 y.lab=Ib y.ax=i2 abs pa

plot.1d	inf=acnpn x.ax=freq x.log x.min=0.0 y.lab=Ib y.ax=i2 points unch pa

end

Output :