|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 B a n d p l a n |  |
| --- | --- | --- |

1.8 MHz

3.5 MHz

Note:   Where the total band available nationally is 100 kHz or less, phone operation
may commence at 3.525 MHz.

7 MHz

10 MHz

14 MHz

Note:   Considering the dramatic increase in data mode usage on the 20 meter band, it is recommended that the sub-band for these classes of signals be 14.070 MHz to 14.112 MHz (with +/- 500 Hz at 14.100 MHz for beacons), and within that data sub-band the current practices of traditional data modes may continue up to 14.095 MHz with 14.095 to 14.112 MHz being reserved for other data modes including Packet.

18 MHz

21 MHz

24 MHz

28 MHz

50 MHz

144 MHz

430 MHz

1,240 MHz

Bands above 1300 MHz:

Societies should consult with the amateur satellite community for proposed satellite operating frequencies before deciding local bandplans above 1300 MHz.

The Basic Principles Underlying the IARU Region 3 Bandplan:

(1) In all cases of conflict between a bandplan and the national regulations of a country, the latter shall prevail.

(2) Nothing in these bandplans shall be construed as prohibiting different national arrangements, provided that harmful interference is not caused to stations in countries operating in accordance with the regional bandplan.

(3) Notwithstanding item 2 above, Member Societies of IARU Region 3 are strongly urged to use these regional bandplans as a basis for their national bandplans.

[Legends]

NB:	Narrow band modes including CW, RTTY, Packet and modes with similar bandwidth not exceeding 2 kHz.

Phone:	Phone operation includes SSTV, FAX and modes with similar bandwidth not exceeding 2 kHz.

WB:	Wide band modes including FM.

Satellite:	This segment should be kept clear of other operating modes.

EME:	Earth-Moon-Earth, Meteor Scatter, Auroral Scatter and other weak-signal.

Secondary:	At 7.1 to 7.3 MHz, amateur stations shall not cause harmful interference to stations of the Broadcasting Service.

____________________

# Text boxes

1,3000

1,240

EME

1,297

1,296

Satellite

1,270

1,260

450

431.9

435

432.240

438

EME

Satellite

430

145.8

146

148

144

144.035

EME

Satellite

50

54

50.1

50.5

Phone and NB

WB

Beacons

CW

28.2

International
Beacon
( 500 Hz
guard band
for beacons

28.0

29.510

28.68 ( 5 kHz
is recommended
for SSTV

29.3

28.050

28.150

28.3

28.190

WB

Satellite

NB

Phone Operation

Beacons

CW

29.7

24.930

International Beacon
( 500 Hz
guard band
for beacons

24.99

24.920

NB

CW

24.89

Phone

21.15

International Becon

( 500 Hz
guard band
for beacons

21.12540

21.070

21.34

( 5 kHz
is recommended
for SSTV

Phone Operation

CW

21.45

21.0

NB

18.110

International Beacon
( 500 Hz
guard band
for beacons

18.068

18.168

18.100

NB

Phone

CW

14.1

International Beacon

( 500 Hz
guard band
for beacons

14.35

14.23

( 5 kHz
is recommended
for SSTV

14.1127.040

14.070

NB

NB

Phone Operation

CW

14.0

10.10

10.157.3

Secondary

NB

10.14

CW

7.0

Secondary

CW

7.3

7.030

7.025

7.040

7.1

NB

NB

Phone Operation

CW

DX

Phone

DX

3.535

3.800

3.775

Phone Operation

CW

3.5

3.9

3.510

RTTY

DX

1.840

1.8

2.0

1.830

1.834

Phone Operation

CW